Specification ISW-621TF

Model ISW-621TF Hardware Specification Copper Ports ‧4 x 10/100Base-TX, Auto-Negotiation, Auto-MDI/MDI-X Cable ‧10Base-T: 2-pair UTP Cat. 3, 4, 5 cable (100meters, max.) ‧100Base-TX: 2-pair UTP Cat. 5, 5e, 6 cable (100meters, max.) Optical Port / Type ‧2 x 100Base-FX / LC Interfaces Cable Mode ‧Multi-mode: 50/125μm / 62.5/125μm fiber ‧Single-mode: 9/125μm fiber Dimension (W x D x H) 135 x 97 x 32 mm Weight 442g Power Requirement 12~48V DC, Redundant power with polarity reverse protection Power Consumption / Dissipation Max. 16 Watts / 54 BTU Installation DIN Rail Kit / Wall Mount Ear Alarm Provides one relay output for power fail Alarm Relay current carry ability: 1A @ DC 24V Switch Specification Switch Processing Scheme Store-and-Forward Address Table 2K entries Buffer 1Mbit Flow Control Back pressure for half duplex IEEE 802.3x Pause Frame for full duplex Switch Fabric 1.2Gbps Throughput (Packet Per Second) 0.89Mpps @ 64Bytes Standards Conformance Standards Compliance IEEE 802.3 Ethernet, 10Base-T IEEE 802.3u Fast Ethernet, 100Base-TX, 100Base-FX IEEE 802.3x Full-Duplex Flow Control Temperature Operating: -40~75 Degree C Storage: -40~85 Degree C Humidity Operating: 5~90% Storage: 5~90% (Non-condensing) Regulation Compliance FCC Part 15 Class A, CE Stability Testing IEC60068-2-32 (Free fall) IEC60068-2-27 (Shock) IEC60068-2-6 (Vibration)