| Model | BSP-300 |
| --- | --- |
| Hardware Specification |
| Network Connector | 3-Port RJ-45 for 10/100/1000Base-T (2-Port with 802.3at / 802.3af PoE injector function) |
| Console Port | 1 x RS-232 DB9 serial port |
| Power Output | 1 x DC out 24@ 2A maximum (two-pin terminal block) |
| LED | System: System (Green) Fault (Green) Per 10/100/1000T RJ-45 Ports: Power LNK/ACT (Green) 1000 (Green) Per PoE Interface: Power LNK/ACT (Green) PoE In-use (Orange) |
| Electrical |
| System voltage ratings | DC 24V |
| Maximum charging current | 15A |
| Max. solar array Voc | DC 60V |
| Max. operating voltage | DC 45V |
| Total current consumption | While operating -32Ma At idle -11mA |
| High temperature shutdown | 100 Degree C disconnect solar and load 80 Degree C reconnect solar and load |
| Overload Capacity | Over 15 Amp will cut off output load |
| Standards Conformance |
| Computer Interface | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX IEEE 802.3ab 1000Base-T IEEE 802.3at / 802.3af for PoE (Power over Ethernet) devices |
| Regulation Compliance | CE, FCC |
| Battery Charging |
| Charge algorithm | Bulk charge (constant current), Absorption charge (constant voltage) and Floating charge. Absorption and Floating charge with PWM protection. |
| Maximum output current | 15A |
| Nickel-cadmium battery | ± 40 mV/Degree Celsius for NiCad type batteries, Charge cut-off @ 55 Degree C (Temperature compensation Baseline@ 25 Degree C) |
| Lead-acid battery (Default Setting) | ± 60 mV/Degree Celsius for lead acid type batteries, Charge cut-off @ 55 Degree C (Temperature compensation Baseline@ 25 Degree C) |
| Float charge voltage | DC 27.2V ( 26.0~30.0V ) |
| Absorption charge voltage | DC 29.2V ( 28.0~32.0V ) |
| LVD (Low Voltage Disconnection) | DC 22.2V ( 21.0~25.0V ) |
| LVR (Low Voltage Reconnection) | DC 24.8V ( 23.0~27.0V ) |
| System Unit |
| Operating Temperature | -20 ~ 60 Degree C |
| Storage Temperature | -40 ~ 90 Degree C |
| Operating humidity | 20% ~ 80% |
| Dimension (W x D x H) | 107.2 x 152 x 65.7 mm |
| Weight | 0.79kg |
| Installation | DIN Rail Kit and Wall Mount Kit |
| Software Utility | Device detect / diagnostic, Windows XP / Win 7 |