| ICA4200V |
| --- |
| Image device | 1/2.9 type Sony Exmor progressive scan CMOS sensor |
| Lens | Vari-Focal 3.3~12.0mm, DC Auto-Iris Mechanical IR Cut Filter Angle of view : horizontal: 27 ~ 82 Degree / vertical: 19 ~ 64 Degree |
| Min Illumination | 0.5 Lux (Color) @ F1.2 0.1 Lux (B/W) |
| IR Illuminations | IR LED x 12, 850nm Built-in IR illuminators, effective up to 20 meters |
| Effective Pixels | 1920 x 1080 pixels |
| Image |
| Video Compression | H.264 / MPEG-4 / M-JPEG |
| Video Resolution | 1080P mode H.264: 1080P / 640 x 360 / 320 x 180 / 160 x 90 M-JPEG: 1080P / 640 x 360 / 320 x 180 / 160 x 90 MPEG4: 1080P / 640 x 360 / 320 x 180 / 160 x 90 720P mode H.264: 1280 x 720 / 640 x 360 / 160 x 90 M-JPEG: 1280 x 720 / 640 x 360 / 160 x 90 MPEG-4: 1280 x 720 / 640 x 360 / 160 x 90 |
| Frame Rate | Up to 30fps for all resolutions |
| Image Setting | AE, AWB 3D Noise reduction WDR Color, brightness, sharpness, contrast Mirror/Flip 10 Privacy Masks Text, time and date overlay Overlay image on video |
| Streaming | Simultaneously multi-profile streaming Streaming over UDP, TCP, HTTP, or HTTPS M-JPEG streaming over HTTP (server push) Supports 3GPP mobile surveillance (MPEG4) Controllable frame rate and bandwidth Constant and variable bit rate (MPEG4/H.264) ROI |
| Audio |
| Audio Streaming | Two-Way Audio |
| Audio Compression | RTSP: G.711 64kbps, G.726 32kbps 3GPP: AMR |
| Microphone | External microphone input |
| Audio Output | Adjustable audio output gain |
| Network and Configuration |
| Standard | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX IEEE 802.3ab 1000Base-T |
| Protocol | IPv4, IPv6, TCP/IP, UDP, HTTP, HTTPS, SMTP, FTP, NTP, DNS, DDNS, DHCP, ARP, Bonjour, UPnP, RTSP, RTP, RTCP, IGMP, PPPoE, 3GPP, ICMP, Samba |
| Security | Password protection, IP address filtering, HTTPS encrypted data transmission, user access log |
| Users | 20 clients on-line monitoring at the same time |
| System Integration |
| Application Programming Interface | Open API for software integration ONVIF Compliant |
| Alarm Triggers | Intelligent Motion / Tampering / Audio detection and external input |
| Alarm Events | File upload via FTP, Samba to NAS, SD card or email Notification via email, HTTP, and TCP External output activation Audio alerting output Go to PTZ preset position |
| Video Buffer | Pre- and post-alarm buffering |
| General |
| Power Requirement | 12V DC, 1A IEEE 802.3af Class 3 |
| Power Consumption | 8W max. |
| Operating Temperature | 0 ~ 50 Degree C |
| Operating Humidity | 20 ~ 80% (non-condensing) |
| Weight | 635g |
| Dimension (Φ x L) | 152 x 109 mm |
| Emission | CE, FCC |
| Connectors | 10/100/1000 Mbps Gigabit Ethernet, RJ-45 DC power jack Terminal block for 1 alarm input and 1 output RS-485 interface for scanners, pan/tilts External MIC input Audio out Composited video out (Max. resolution: D1 720 x 480 pixel)) Micro SD/SDHC card (Max 32GB, Class 6) Factory default reset |
| Photo | Model | Description |