Specification

Model IGS-10020MT Hardware Specification Copper Ports 8 10/ 100/1000Base-T RJ-45 Auto-MDI/MDI-X ports SFP/mini-GBIC Slots 2 1000Base-SX/LX/BX SFP interfaces (Port-9 and Port-10) Compatible with 100Base-FX SFP Switch Architecture Store-and-Forward Switch Fabric 20Gbps / non-blocking Throughput (packet per second) 14.8Mpps Address Table 8K entries, automatic source address learning and ageing Share data Buffer 512 kilobytes Flow Control IEEE 802.3x Pause Frame for Full-Duplex Back pressure for Half-Duplex Jumbo Frame 9Kbytes Reset Button < 5 sec: System reboot > 5 sec: Factory Default ESD Protection 6KV DC EFT Protection 6KV DC Enclosure IP30 Aluminum Metal Case Installation DIN Rail Kit and Wall Mount Kit Alarm One relay output for power fail. Alarm Relay current carry ability: 1A @ DC 24V LED Indicator System: Power 1 (Green) Power 2 (Green) Fault Alarm (Green) Per 10/100/1000T RJ-45 Ports: Power LNK/ACT (Green) 1000 (Orange) Per SFP Interface: Power LNK/ACT (Green) 1000 (Orange) Dimension (W x D x H) 87.8 x 135 x 56 mm Weight 720g Power Requirement DC 12 to 48V. AC 24V Power Adapter Power Consumption 10 Watts / 34BTU (Full loading) Layer 2 function Basic Management Interfaces Web Browser, Remote Telnet, SNMPv1, v2c Secure Management Interface SSH, SSL, SNMP v3 Port configuration Port disable / enable Auto-Negotiation 10/100/1000Mbps full and half duplex mode selection Flow Control disable / enable Power saving mode control Port Status Display each port’s speed duplex mode, link status, Flow control status, Auto negotiation status, trunk status Port Mirroring TX / RX / Both Many-to-1 monitor VLAN 802.1Q Tagged Based VLAN, up to 255 VLAN groups Q-in-Q tunneling Private VLAN Edge (PVE) MAC-Based VLAN Protocol-Based VLAN Voice VLAN MVR (Multicast VLAN Registration) Up to 255 VLAN groups, out of 4095 VLAN IDs Link Aggregation IEEE 802.3ad LACP / Static Trunk 5 groups of 10-Port trunk support QoS Traffic classification based, Strict priority and WRR 8-level priority for switching - Port Number - 802.1p priority - 802.1Q VLAN tag - DSCP/TOS field in IP Packet IGMP Snooping IGMP (v1/v2/v3) Snooping, up to 255 multicast Groups IGMP Querier mode support MLD Snooping MLD (v1/v2) Snooping, up to 255 multicast Groups MLD Querier mode support Access Control List IP-Based ACL / MAC-Based ACL Up to 123 entries Bandwidth Control Per port bandwidth control Ingress: 500Kb~80Mbps Egress: 64Kb~80Mbps SNMP MIBs RFC-1213 MIB-II IF-MIB RFC-1493 Bridge MIB RFC-1643 Ethernet MIB RFC-2863 Interface MIB RFC-2665 Ether-Like MIB RFC-2819 RMON MIB (Group 1, 2, 3 and 9) RFC-2737 Entity MIB RFC-2618 RADIUS Client MIB RFC-2933 IGMP-STD-MIB RFC-3411 SNMP-Frameworks-MIB IEEE 802.1X PAE LLDP MAU-MIB Standards Conformance Regulation Compliance FCC Part 15 Class A, CE Stability Testing IEC60068-2-32 (Free fall) IEC60068-2-27 (Shock) IEC60068-2-6 (Vibration) Standards Compliance IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX / 100Base-FX IEEE 802.3z Gigabit SX/LX IEEE 802.3ab Gigabit 1000T IEEE 802.3x Flow Control and Back pressure IEEE 802.3ad Port trunk with LACP IEEE 802.1D Spanning Tree Protocol IEEE 802.1w Rapid Spanning Tree Protocol IEEE 802.1s Multiple Spanning Tree Protocol IEEE 802.1p Class of service IEEE 802.1Q VLAN Tagging IEEE 802.1x Port Authentication Network Control IEEE 802.1ab LLDP RFC 768 UDP RFC 793 TFTP RFC 791 IP RFC 792 ICMP RFC 2068 HTTP RFC 1112 IGMP version 1 RFC 2236 IGMP version 2 RFC 3376 IGMP version 3 RFC 2710 MLD version 1 FRC 3810 MLD version 2 Environment Operating Temperature: -40 ~ 75 Degree C Relative Humidity: 5 ~ 95% (Non-condensing) Storage Temperature: -40 ~ 75 Degree C Relative Humidity: 5 ~ 95% (Non-condensing)