Specification IGTP-80xT Series

Model IGTP-80xT Series Hardware Specification 10/100/1000Base-T Port 1-Port RJ-45 interface, auto-negotiation and auto MDI / MDI-X 1000Base-X Fiber Interface IGTP-802T: SC IGTP-802TS: SC IGTP-805AT: SFP (LC) Fiber Cable IGTP-802T Multi-mode: 50/125um or 62.5/125um optic fiber IGTP-802TS Single-mode: 9/125um optic fiber IGTP-805AT Vary on SFP Module Cable Distance IGTP-802T: 220m / 550m IGTP-802TS: 10km IGTP-805AT: Vary on SFP Module Optical Frequency IGTP-802T: 850nm IGTP-802TS: 1310nm IGTP-805AT: Vary on SFP Module Launch Power IGPT-802T: Max. -4dBm Min. -9.5dBm IGTP-802TS: Max. -3dBm Min. -9.5dBm IGTP-805AT: Vary on SFP Module Receive Sensitivity IGTP-802T: -13.5dBm IGTP-802TS: -14.4dBm IGTP-805AT: Vary on SFP Module Maximum Input power IGTP-802T: -18dBm IGTP-802TS: -20dBm IGTP-805AT: Vary on SFP Module IEEE 802.3at / 802.3af PoE Port 1, End-Span, 1/2(+), 3/6(-) LED Indication System: Power 1, Power 2 and Fault LED (Green) Fiber port: LNK / ACT (Green) 10/100/1000Base-T port: LNK / ACT, PoE In-use (Green / Orange) Link Fault Pass-Through DIP Switch ON / OFF Flow Control Back pressure for half duplex, IEEE 802.3x Pause Frame for full duplex Maximum Frame Size 9216 bytes Power Requirement 24VDC or 48VDC, redundant power with polarity reverse protect function Enclosure IP30 Aluminum metal case Dimension (W x D x H) 135 x 87 x 32mm Weight IGTP-802T / IGTP-802TS: 510g IGPT-805AT: 500g Installation DIN rail kit and wall mount ear ESD Protection 6KV DC EFT Protection 6KV DC Alarm Provides one relay output for power fail Alarm Relay current carry ability: 1A @ DC 24V Speed Twisted-pair: 10/20Mbps for Half / Full-Duplex, 100/200Mbps for Half / Full Duplex 1000/2000Mbps for Full Duplex Fiber-Optic: 200Mbps / 2000Mbps for Full-Duplex Network Cables 10/100/1000Base-T: 2-Pair UTP Cat. 3, 4, 5, 5e, 6 (Maximum 100 meters) EIA / TIA-568 100-ohm STP (Maximum 100 meters) 100Base-FX / 1000Base-SX / LX: Multi-mode: 50/125um or 62.5/125um optic fiber Single-mode: 9/125um optic fiber Power Consumption 24V: 33 Watts / 112BTU, 48V: 31 Watts / 105BTU (With PoE) Power over Ethernet PoE Standard IEEE 802.3af / 802.3at High Power over Ethernet / PSE PoE Power Supply Type End-Span PoE Power Output 52V DC. 15.4 Watts 52V DC. 30 Watts Power Pin Assignment 1/2(+), 3/6(-) Standards Conformance Standards Compliance IEEE 802.3 10Base-T Ethernet IEEE 802.3u 100Base-TX / FX Fast Ethernet IEEE 802.3ab 1000Base-T Gigabit Ethernet IEEE 802.3z 1000Base-SX / LX Gigabit Ethernet IEEE 802.3x Full-Duplex Flow Control IEEE 802.3af Power over Ethernet IEEE 802.3at High Power over Ethernet Stability Testing IEC60068-2-32 (Free fall) IEC60068-2-27 (Shock) IEC60068-2-6 (Vibration)