| Hardware Specification WDL-U700 |
| --- |
| Interface | USB 2.0, Type-A |
| Antenna Type | Internal antenna |
| LED | 1 x Link / Active (Amber) |
| Operation Voltage | 5V DC, power input from USB port |
| Dimension (W x D x H) | 24 x 86 x 10 mm with USB cap 24 x 83 x 10 mm without USB cap |
| Wireless Specification |
| Standards Conformance | IEEE 802.11n standard compliant IEEE 802.11b/g backwards compatible IEEE 802.11a backwards compatible |
| RF Modulation | BPSK, QPSK, CCK OFDM (BPSK/QPSK/16-QAM/ 64-QAM) |
| Frequency Band | 2.4-2.4835 GHz 5.180~5.240GHz 5.260~5.320GHz 5.745~5.825GHz |
| Operating Channel | 802.11a/n USA/Canada: 24 non-overlapping channels Major Europe Countries: 19 non-overlapping channels Japan: 19 non-overlapping channels China: 5 non-overlapping channels 802.11b/g/n USA/Canada: 11 (1-11) Major Europe Countries: 13 (1-13) France: 4 (10-13) Japan: 14 for 802.11b (1-13 or 14th), 13 for 802.11g (1-13) China : 13 (1-13) |
| Data Rate | 802.11a: 54, 48, 36, 24, 18, 12, 9 and 6Mbps 802.11b: 11, 5.5, 2 and 1 Mbps with auto-rate fall back 802.11g: 54, 48, 36, 24, 18, 12, 9 and 6Mbps 802.11n (20MHz): up to 144.4Mbps 802.11n (40MHz): up to 300Mbp |
| Wireless Transmit Power (EIRP) | 20dBm (max) |
| Receiver Sensitivity | IEEE 802.11n HT40: -61dBm@10% PER IEEE 802.11n HT20: -64dBm@10% PER IEEE 802.11g: -65dBm@10% PER IEEE 802.11b: -85dBm@8% PER IEEE 802.11a: -65dBm@10% PER |
| Operating Mode | Ad-Hoc / Infrastructure, Soft AP |
| Encryption Security | WEP 64/128-bit WPA / WPA2 (TKIP/AES) WPA-PSK / WPA2-PSK (TKIP/AES) |
| Wireless Advanced | Supports 802.11e WMM (Wi-Fi Multimedia) Supports Software WPS (Wi-Fi Protected Setup) |
| Management | The utility included in the package or Windows XP Zero Configuration utility |
| Operating Systems | Windows 2000/XP (x86/x64) / VISTA (x86/x64) / Win7 (x86/x64) Linux Kernel 2.4 /2.6 Macintosh 10.4/10.5/10.6/10.7/10.8 |
| Certification |
| Emission | CE, FCC |
| Environment |
| Operating Temperature | 0 ~ 40 Degree C (32 ~ 104 Degree F) |
| Humidity | 10 ~ 90%, non condensation |
| Package | WDL-U700 (300Mbps 802.11n Wireless USB adapter) Quick Installation Guide CD (includes driver, utility, user’s manual) |